DACAP - Distance Aware Collision Avoidance Protocol

RTS/CTS:
nodeA RTS -> nodeB
nodeB CTS -> nodeA
nodeA data -> nodeB
nodeB ack -> nodeA
nodes overhearing RTS or CTS keep silent during time period indicated by the RTS & CTS

Leveraging of long propagation delays:
During a time period after a RTS is sent out and before a CTS is received, the RTS sender and it's neighbors may perform other actions (transmitting data or handshaking). This will not always be effective depending on traffic load and long access delays will always be an issue.
A frame coming from a far away node may not corrupt a frame coming from a closer node if they are transmitted with the same power. Close nodes may handshake without worrying about interference from remote transmissions. DACAP exploits the differences in distances between nodes to set handshaking lengths instead of using waiting times proportional to the maximum inter-node distance.
Designed for underwater networks with long propagation delays.